## Slide 1
ALT Series Ultrasonic Cleaner
Model | ALT-2545-1200-82H
Functional | 
Frequency (kHz) | 2545
Capacity (Litres) | 82
Ultrasonic Power (Watts) | 1200
Sweeping Function | Yes
Power Intensity | 10 - 100% Adjustable
Timer Function | 1 - 60 mins / Infinity
Immersion Heater Power (Watts) | 1500
Temperature Sensor Type | PT100
Temperature Range (Celsius) | 20 – 70 °C
Connected Power (Ampere) | 13
Input Power | AC 220 – 240 V, Single Phase, 50/60Hz
Programmable HMI (Touchscreen) | Not Applicable
Physical | 
Internal Tank Dimension L x W x H (mm) | 550 x 300 x 500
Overall External Tank Dimension w/o Valve (mm) | 622 x 530 x 793 (+ 100 mm with Base Support)
Internal Tank Material | SS316L
External Tank Material | SS304
Net Weight (kg) | 80
Water Inlet Valve | SS316, ½ Inch Full Ball Valve
Drainage Valve Material | SS316, 1 ¼ Inch Full Ball Valve
Power Cable Length | 3m with Quick Connector and 5-Pin Wall Plug
Basket | 
Basket Internal Dimension L x W x H (mm) | 518 x 268 x 420
Basket Material | SS316L
Mesh Grid Size (mm²) | 25 x 25
Optional | 
High Density Basket Model | ABK-2545-1200-82-01
Mesh Grid Size (mm²) | 5 x 5
www.alstron.com.sg sales.sg@alstron.com.sg
ALT-2545-1200-82H
Signature Frequency 2545kHz for General Cleaning Applications
Internal Tank - Stainless Steel SS316L, External Tank - SS304 Construction
Adjustable Digital Timer for Ultrasonic Duration Control
Digital Temperature Controller for Heating Control
Sweeping Function & Adjustable Ultrasonic Power Intensity
PLL Technology with Auto-Frequency Tracking & Adjustment
Strong Holding Basket in SS316, 1 square-inch Mesh
Power Input: AC 220 – 240V, Single-Phase
Water Drainage Piping & Valve in SS316
SS316L Base Structure for Vessels (optional Castor Wheel with Brakes for Easy Transportation)
Alstron ALT Series Ultrasonic Cleaner provides a comprehensive range of units tailored for industrial part cleaning. Applications cover degreasing and removing contaminants from various components including marine vessels, aerospace parts, PCBs, machining parts, mechanical components (pre-coating or plating), optical parts, surgical instruments, 3D modeling, R&D, and more.